## Slide 1: Radio Direction Finding
Gloucester County NJ Amateur Radio Club Jim, N2GXJ
1

## Slide 2: What is RDF?
2
• RDF – Radio Direction Finding
– Determining the direction from which a received radio signal was transmitted.
• Technology has changed over the decades
• Essential elements of the techniques have not
• Success is still largely up to the skill of the RDF equipment operator

## Slide 3: When RDF?
3
• Searching for sources of radio interference
• Localizing non-authorized transmitter
• Identification of transmitters, known and unknown
• Dealing with spread spectrum techniques, especially in wireless communications
• Military and security forces
• Civilian search and rescue
• Wildlife tracking
• Radiosport!

## Slide 4: History
• DF technique is as old as radio
• Heinrich Hertz (1888) experiments with decimetric waves found antenna directivity
• Early patents
– Stone, 1902
– Forest, 1909
– Belini and Tosi, 1909
– Adcock, 1919
4

## Slide 5: History -WWI
• DF widely used to pinpoint enemy
forces during WWI
• “Radio Compass”, prototype for
U.S. Navy 1916
• Passive technology, listen in on
large military forces keeping in
contact with their headquarters
• Manual RDF techniques
– Rotatable antennas
• RF propagation challenges,
groundwave, skywave, multi-path,
fading, polarization changes,
non-white external noise, seasonal
and time-varying ionospherics,
(don’t we know!)
Kensington Maryland field station, circa 1919, NIST Photographic Collection
(http://museum.nist.gov/panels/gallery/radiodf.html)
5

## Slide 6: History - WWII
• Accuracy improvement – HF/DF Nets
– Multiple RDF stations operating together as a “net”
– Each try get directional fix on callsign heard, noting time and frequency, then coordinate with others
– Intercept lines drawn on map for all sites that got a fix on target
Ref: http://www.researcheratlarge.com/Pacific/RDF/
6

## Slide 7: WWII, RDF Stories
• Pearl Harbor
– As shown in movie “Tora Tora Tora”, Japan fleet used Honolulu
broadcast station as an over-the-horizon beacon for attack on
Pearl Harbor
– Regular Japanese carrier radio operators kept back in Tokyo,
generating false traffic
• their unique styles recognized and located as being in home islands
• Secret Transmitters
– British Radio Security Service – up to 1700 volunteer interceptors (radio amateurs) recruited to detect illicit transmissions
– Similar efforts in Europe by the Germans to locate resistance groups
• D-day Deceptions
– Operation Fortitude, with (fake) First US Army Group, led by
George Patton. Radio trickery helped convince Germans real plan for
invasion in Calais, not Normandy.
• U-boats
– U-boat “loop” antenna technology, used in hunting Allied shipping (ref: http://uboat.net/articles/51.html)
– British ships outfitted with new automatic “HuffDuff” very
effective in tracking and hunting short duration German
submarine transmissions, helped turn the tide of shipping losses
U.S. Navy DAQ (WWII)
German EP2a
German U-67 DF Antenna
7

## Slide 8: Cold War
• After WWII
– From 1950’s, US adapted German Wullenweber antenna systems for use in Vietnam, cold-war eavesdropping (FRD-10, AN/FLR-9)
– Russians deployed similar (Krug), early use included tracking Sputnik
– OUTBOARD HF/DF systems standardized on U.S. Navy vessels
• New and Improved Technologies
– Automatic signal search and analysis
– Combined active/passive systems (e.g. Over the horizon HF radar)
8
Refs: http://www.answers.com/topic/radio-direction-finding-equipment AN/FLR-9, ref: http://en.wikipedia.org/wiki/Wullenweber http://www.engineeringradio.us/blog/2010/10/how-the-cold-war-was-won

## Slide 9: Modern Era
• Military (still)
• Search and Rescue
• Wildlife Tracking
• Spectrum enforcement
• Amateur RDF

## Slide 10: Search and Rescue
• Distress Radio Beacons
– Maritime (EPIRBs)
– Aircraft (ELTs)
– Personal (PLBs)
• What about APRS(average packet
delivery radio system) ?
– Has distress packet type, but not guaranteed & not satellite compatible
• Cospas-Sarsat (satellite) compatible
beacon frequencies
– 406.025 Mhz (digital burst, satellite)
– 121.5 MHz (analog, short range homer)
– 243. Mhz (old, phased out since 2009)
• Other systems, not so standard
– 457 kHz, Avalanche transceiver
– 216-217 MHz, LoJack ‘Safetynet’ & law enforcement tracking devices

## Slide 11: Wildlife Tracking
• Tracking
– Micro-transmitters, collars, tagging technologies
– RDF techniques (fixed-wing, mobile, and on-foot)
• Studies
– Migration patterns
– Population studies
• Volunteer opportunities?

## Slide 12: RDF Technologies
• Spectrum Enforcement
– If can’t ID interfering signal by demodulation, or signal analysis, need radiolocation to locate source
• Radiolocation Technologies
– Manual Techniques
– Doppler DF
– Watson-Watt
– Time difference of arrival, SRDF(super resolution DF)

## Slide 13: RDF Technology
• Manual Techniques
– Use of receiver and hand-held directional
antenna
– Antenna is moved/rotated to find
directions of min and max signal strength,
usually based on signal amplitude
– “Home-in” on signal by moving in
direction of signal, then sweep to test
possible locations in suspect area
– Can also plot bearing lines to triangulate general transmitter location
– Limitations: highly dependent on skill of operator, accuracy poor at distance,
difficult to get bearing on short duration
signals, difficult to get bearing on
frequency agile signals
Rohde & Schwarz portable monitoring & RDF

## Slide 14: Homing-in by Bearing
• If mobile, can take bearing, follow it for a bit, then repeat
• Not always shortest path

## Slide 15: Triangulation
• Narrow search area by triangulating lines of bearing
– Take directional measurements from several locations
– Plot bearings on a map, narrow search to where bearings intersect
– Directional uncertainty at distance, progressively smaller hunt areas
– Max signal strength (S-meter) when close, attenuate to avoid overload

## Slide 16: Watson-Watt
• Amplitude comparison
technique, developed after WWII, using crossed loop, or Adcock antennas
• Enabled real-time RDF, even for short duration signals
• Difference signals from N-S, and W-E used to deflect electron beam on CRT
• Basic Adcock/Watson-Watt design is basis of many
systems today

## Slide 17: TDOA
• Time difference of arrival (TDOA)
• Works on detecting a phase difference, not amplitude difference
– Useful for close-in work, when amplitude schemes overload
• FM tone when signal not arriving at antennas at same time
– Turn antenna unit until find null (180 degree ambiguity)

## Slide 18: Doppler DF
• Doppler shift
– Circular array, electrically rotating antenna
(goniometer = 각도계, CDAA=cirularly disposed antenna array)
– Single receiver, rotational FM tone demodulated
– Closer to signal: frequency shifts up, away: shift down
– Phase offset of recovered tone vs. original is direction of arrival

## Slide 19: Correlation Interferometer(CI) RDF
• Interferometry first used in radio astronomy
• Measures angle of incident wavefront at multiple elements
• Relies on digital signal processing for sensor array processing
• Electrically small active or passive elements, wideband performance
• Number of elements in CI antenna varies (5-9 typical)

## Slide 20: TDOA / Super-resolution / SRDF
• Taking advantage of software - digital signal processing techniques
– Since 1990’s, order of magnitude increase in resolution
– Increased DF accuracy
– Azimuth and elevation DF
– Simultaneous DF of multiple co-channel signals
– Operation with very few data samples (MUSIC, Capon, ESPRIT algorithms)
– Adaptive beam forming for signal separation (null steering)
– Not fixed to a particular array geometry (array manfold from stored
calibration function)

## Slide 21: Digital receivers
• Near instantaneous signal acquisition
• No calibration required
• No need for multiple coherent local oscillators
• Supports DF on short duration / frequency hopping signals
• Supports reconstruction of frequency hoppers
• Broadband beam forming without need for large coaxial cable delay lines
• N channels provides 10logN dynamic range enhancement
Ref: http://www.g4axx.com/HF_Radio_Direction_Finding.pdf

## Slide 22: Digital Beam forming
• You might have digital beam forming equipment in your home or office right now!
• 802.11n WI-FI since 2009 (e.g. Cisco Aironet, Ruckus 7962)
– Adaptive antenna technology
– Null steering for automatic interference mitigation

## Slide 23: Radio Direction Finding
• Thank you! See you!