## Slide 1
Frequency Bands

## Slide 2
I. Frequency Bands
1. ITU bands
2. ECM bands
3. EU/NATO radio bands alternative
4. IEEE radio bands
5. Waveguide frequency bands

## Slide 3
1. ITU (International Radio Union) bands
1 (ELF) 3-30 Hz
2 (SLF) 30-300 Hz
3 (ULF) 0.3-3 kHz
4 (VLF) 3-30 kHz
6 (LF) 30-300 kHz
7 (MF) 0.3-3 MHz
8 (HF) 3-30 MHz
9 (VHF) 30-300 MHz
10 (UHF) 0.3-3 GHz
11 (SHF) 3-30 GHz
12 (EHF) 30-300 GHz
13 (THF) 0.3-3 THz

## Slide 4
2. ECM bands (EU/NATO/US)
A 0 – 250 MHz
B 250-500 MHz
C 0.5-1 GHz
D 1-2 GHz
E 2-3 GHz
F 3-4 GHz
G 4-6 GHz
H 6-8 GHz
I 9-10 GHz
J 10-20 GHz
K 20-40 GHz
L 40-60 GHz
M 60-100 GHz

## Slide 5
3. EU/NATO radio bands alternative
I 100-150 MHz
G 150-225 MHz
P 225-400 MHz
L 0.39-1.55 GHz
S 1.55-3.90 GHz
C 3.9-6.2 GHz
X 6.2-10.9 GHz
K 10.9-36.0 GHz
Ku 10.9-20 GHz
Ka 20-36 GHz
Q 36-46 GHz
V 46-56 GHz
W 56-100 GHz

## Slide 6
4. IEEE radio bands
HF 3-30 MHz
VHF 30-300 MHz
UHF 0.3-3 GHz
L 1-2 GHz
S 2-4 GHz
C 4-8 GHz
X 8-12 GHz
Ku 12-18 GHz
K 18-27 GHz
Ka 27-40 GHz
V 40-75 GHz
W 75-110 GHz
mm 30-300 GHz

## Slide 7
5. Waveguide frequency bands
R 1.70-2.60 GHz
D 2.20-3.30 GHz
S 2.60-3.95 GHz
E 3.30-4.90 GHz
G 3.95-5.85 GHz
F 4.90-7.05 GHz
C 5.85-8.20 GHz
H 7.05-10.10 GHz
X 8.2-12.4 GHz
Ku 12.4-18.0 GHz
K 15.0-26.5 GHz
Ka 26.5-40.0 GHz
Q 33-50 GHz
U 40-60 GHz
V 40-75 GHz
W 75-110 GHz
F 90-140 GHz
D 110-170 GHz
G 140-220 GHz
Y 325-500 GHz

## Slide 8
II. ITU Regions
1. ITU
2. ITU radio spectrum regions

## Slide 9
1. ITU (International Telecommunication Union)
- 국제전기통신연합
- 유엔 산하 기구. 전기통신 관련 국제협력
- ITU-R (무선통신): 1927년 출범
- ITU-T (표준화): 1956년 출범
- ITU-D (개발): 1992년 출범
- ITU Telecom (행사): 1971년 출범. ITU Telecom World 2011 (40주년)
- WRC (규정, 협약): World Radiocommunication Conferences
3-4년 주기로 개최. 주파수 사용, 정지/비정지 위성궤도 관련 국제
규약의 심의, 개정, 제정

## Slide 10
2. ITU radio spectrum regions

## Slide 11
III. Frequency per Applications
1. Broadcast frequencies
2. GNSS frequencies
3. Aeronautical telemetry frequencies (WRC'07)

## Slide 12
1. Broadcast frequencies
Longwave AM Radio 148.5-283.5 kHz
Medium Wave AM Radio 530-1710 kHz
Shortwave AM Radio 3-30 MHz
FM Radio
87.5-108.0 MHz (ITU Region I)
87.9-107.9 MHz (ITU Region II)
76.0-90.0 MHz (Japan)
TV 54- 698 MHz
Americas, Caribbean, South Korea, Taiwan, the Philippines
54-88 MHz VHF Low-band (Band I), ch. 2-6
174-216 MHz VHF High-band (Band III), ch. 7-13

## Slide 13
1. Broadcasting frequencies
Band I 47-88 MHz
Band II 87.5-108.0 MHz
Band III 174-250 MHz
Band IV 474-602 MHz (BBC)
Band V 614-854 MHz (BBC)
Band VI 11.7-12.7 GHz

## Slide 14
2. GNSS frequencies

## Slide 15
3. Aeronautical telemetry frequencies (WRC'07)
Ref: M. Rice, DTIC, AD578383

## Slide 16
4. Short range devices (SRDs)
A) All
3.155-3.195 MHz Hearing aids
6.765-6.795 MHz ISM, non-specific
13.553-13.567 MHz ISM, RFID, NFC
26.957-27.283 MHz Citizen's band
315-316 MHz China
40.669-40.700 MHz ISM, non-specific
260-470 MHz Canada
402-405 MHz ISM, Active medical implants
433.050-434.790 MHz ISM, LPD433
863-870 MHz SRD860
902-928 MHz Canda
915-928 MHz Australia

## Slide 17
2.400-2.4835 GHz Wi-Fi, amateur radio
5.725-5.875 GHz ISM
5.795-5.805 GHz Automatic toll collection
5.805-5.815 GHz Automatic toll collection
76-77 GHz Automotive long range radar (LRR)
61.0-61.5 GHz ISM
122-123 GHz ISM
244-246 GHz ISM

## Slide 18
B) Global license-free SRD frequencies in MHz
Europe: 433.05-434.79, 868.0-870.0, 863.0-870.0
U.S.: 260-470, 902-928
Canada: 260-470, 902-928
Japan: 426.0375-426.1125, 429.175-429.7375
China: 315.0-316.0, 430.0-432.0
Austalia: 433.05-434.79, 915-928

## Slide 19
C) 대한민국 소출력 무선기기
코드없는 전화기: 3mW = 46.510-46.970MHz/49.695-49.970MHz
10mW = 914.01-914.9875MHz/959.0125-959.9875MHz
특정 소출력: 10mW = 219.000-224.125MHz, 10mW = 424.700-424.950MHz
무선마이크:
3mW: 74MHz 대역
1mW: 106-107MHz 대역
3mW: 220MHz 대역
10mW: 740-750MHz 대역
10mW: 928-929MHz 대역
무선조정용:
10mW: 173MHz 대역, 산업용(중장비, 크레인)
5mW: 173MHz 대역, 447MHz 대역, 자동문 제어, 자동차 시동
5mW: 311MHz 대역, 자동차 시동
안전시스템:
10mW: 447MHz 대역, 도난/화재 경보장치

## Slide 20
영상전송용:
10mW = 2.410-2.470GHz
시각 장애인 유도신호용:
235MHz: 고정장치, 10mW
358MHz: 휴대장치, 10mW
ISM 대역
13.560MHz: 교통카드, 모형기기 무선조정
27.120MHz: 생활무선국, 모형기기 무선조정
40.690MHz: 모형기기 무선조정
915MHz: 국가 사용
2.450GHz: 아마추어, 이동체 식별장치, 무선LAN
5.800GHz: 아마추어, 방송중계, 군레이더, 무선LAN
24.125GHz: 아마추어, 고주파 이용설비

## Slide 21
국내 허가/신고 불필요 무선주파수
322MHz 미만: 500μV/m 이하. 15MHz 이하에서는 6π/λ를 곱함.
322MHz 이상 10GHz 미만: 35μV/m 이하
10GHz 이상 150GHz 미만: 3.5f μV/m, f(GHz), 500μV/m 초과시 500μV/m로 한다.
150GHz 이상: 500μV/m 이하

## Slide 22
US Amateur Radio Frequency Allocation
송신출력 상한선: 1.5 kW PEP, 200 W PEP on HF bands
160-m 1.8-2.0 MHz
80-m 3.5-4.0 MHz
60-m 5.332-5.4035 MHz
40-m 7.025-7.300 MHz
30-m 10.10-10.15 MHz
20-m 14.025-14.350 MHz
17-m 18.068-18.168 MHz
15-m 21.025-21.450 MHz
12-m 24.890-24.990 MHz
10-m 28.0-29.7 MHz
6-m 50.0-54.0 MHz
2-m 144.0-148.0 MHz
1.25-m 222-225 MHz
70-cm 420-450 MHz
33-cm 902-928 MHz
23-cm 1270-1295 MHz

## Slide 23
US Amateur Radio Frequency Allocation
Higher Frequencies (GHz):
2.30-2.31
2.39-2.45
3.30-3.50
5.65-5.925
10.0-10.5
24.0-24.25
47.0-47.2
76.0-81.0 (76-77 GHz suspended due to vehicle radar interference)
122.25-123
134-141
241-250
All above 300

## Slide 24
Radio Astronomy Frequencies (Europe)
1. MHz band
13.35-13.41
22.55-25.67
37.5-38.25
73-74.6
150.05-153
322-328.6
406.1-410
608-614
2. GHz band
1.4-1.427
1.66-1.6605
1.6605-1.6684
1.6684-1.670
1.7188-1.7222
2.655-2.690

## Slide 25
Radio Astronomy Frequencies (Europe)
2. GHz band
2.69-2.70
3.260-3.267
3.332-3.339
3.3458-3.3525
4.80-4.99
4.99-5.00
5.00-5.03
6.6500-6.6752
10.60-10.68
14.47-14.50
15.20-15.35
15.35-15.40
22.01-22.21
22.21-22.50
22.71-22.86
23.07-23.12

## Slide 26
Radio Astronomy Frequencies (Europe)
2. GHz band
23.6-24.0
31.2-31.3
31.3-31.5
36.43-36.50
42.5-43.5
48.94-49.04
51.40-54.25
58.2-59.0
72.77-72.91
86-92
92-94
95-100

## Slide 27
Cellular Phone Frequencies
Current / Planned Technologies | Previous Technologies | Band | UHF Frequency (MHz)
3G, 4G, MediaFLO (defunct), DVB-H | UHF TV 52-69 (698-806 MHz)* | 700 | 698–806
SMR iDEN, ESMR CDMA (future), ESMR LTE (future) | UHF TV 70-83 (806-890 MHz) | 800 | 806–824 and 851–869
GSM, IS-95 (CDMA), 3G | AMPS, IS-136 (D-AMPS) | 850 | 824–849 and 869–894
Unknown |  | 1400 | 1392–1395 and 1432–1435
GSM, IS-95 (CDMA), 3G, 4G | IS-136 (D-AMPS) | PCS | 1850–1910 and 1930–1990
3G, 4G |  | AWS | 1710–1755 and 2110–2155
4G |  | BRS/EBS | 2496–2690

## Slide 28
Radar Frequency Usage [US DoC, NTIA Special Pub. 00-40]

## Slide 29
Radar Power [US DoC, NTIA Special Pub. 00-40]

## Slide 30
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]

## Slide 31
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]

## Slide 32
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]

## Slide 33
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]

## Slide 34
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]

## Slide 35
Satellite Frequencies
UHF-band
- Shuttle Orbiter UHF System: backup for the S-band and Ku-band
systems. 243.0, 259.7, 296.8 MHz

## Slide 36
Satellite Frequencies
L-band (1–2 GHz)
- GPS: 1.164-1.300 GHz, 1.544-1.610 GHz
- Satellite mobile phone
Iridium: 1.616-1.6265 MHz
Immarsat: 1.525-1.6465 MHz
Thuraya: 1.525-1.661 MHz
- WorldSpace satellite radio (DAB): 1.452-1.492 GHz
- MSS, BGAN, FleetBroadband, Global Handheld Satellite Phone:
up 1.6264-1.6605 GHz, down 1.525-1.559 GHz
- COSPAS-SARSAT: search and rescue satellite radiolocation system

## Slide 37
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]
S-band (2–4 GHz)
- Deep space bands: uplink 2.11-2.12 GHz, downlink 2.29-2.30 GHz
- Near earth bands: uplink 2.025-2.110 GHz, downlink 2.20-2.29 GHz
- MSS (Mobile Satellite Service): 2.0-2.2 GHz
- Digital Audio Radio Service (DARS): 2.31-2.36 GHz
- Earth-to-space communication: 1.98-2.01 GHz
- Space-to-earth communication: 2.17-2.20 GHz
- Direct-to-Home satellite TV: 2.5-2.7 GHz
- Space Shuttle Orbiter S-band system (STDN, TDRS): 1.7-2.3GHz
- WIDESTAR II mobile satellite comm.: uplink 2.66-2.69 GHz,
downlink 2.505-2.535 GHz

## Slide 38
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]
X-band (8-12 GHz)
- Space communication
Deep space bands: up 7.145-7.190 GHz, down 8.40-8.45 GHz
Near earth bands: up 7.190-7.235 GHz, down 8.45-8.50 GHz
- Military communication: COTM (communications-on-the-move)
up 7.9-8.4 GHz, down 7.25-7.75 GHz
NATO SATCOM Post-2000
- Civilian communication:
Skynet
Wideband Global SATCOM (WGS),
XTAR-EUR
Spainsat
Sicral, Syracuse,
DC-MS Series 2

## Slide 39
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]
Ku-band (12–18 GHz)
- Space communication
Shuttle Orbiter Ku-band System: 15.25-17.25 GHz
- Civilian communication: direct broadcast
up 14 GHz, down 10.70-12.75 GHz

## Slide 40
Radar Frequency Usage [US DoC, NTIA Specil Pub. 00-40]
Ka-band (26–40 GHz)
- Military: up 30.0-31.0 GHz, down 20.2-21.2 GHz
- Civilian: up 27.5-30.0 GHz, down 17.7-20.2 GHz
VSAT: up 29.6-30.0 GHz, down 19.8-20.2 GHz